## Slide 1: IETF Hackathon
IPWAVE Basic Protocols Project Champion: Jaehoon Paul Jeong pauljeong@skku.edu
Sungkyunkwan University
IETF 108
July 20-24, 2020
Online

## Slide 2: Hackathon Plan
Provide a Context-Aware Navigator Protocol (CNP) for IP Based Vehicular Networks:
    Proof of Concept (POC) of IPv6-Based Context-Aware Navigator Protocol
    IPv6 mobility information sharing for safe driving in roadways
    Coordinated path planning for obstacle and collision avoidance in roadways
    Efficient driving information exchange in IP-based vehicular networks
    Network-based coordinated driving environment sensing and perception
Proving strategy:
  Vehicular Simulations of IPWAVE with OMNeT++, SUMO, and VEINS

## Slide 3: Context Awareness in IP-Based Vehicular Networks
Context Awareness in IP based Network
Via lightweight messages Cooperative Context Messages (CCM)
Emergency Context Message (ECM)
CCM
ECM

## Slide 4: Vehicle Mobility Information
VMI options:
Type: Either: CCM and ECM
1
0
9
8
7
6
5
4
3
2
1
0
9
8
7
6
5
4
3
2
1
0
9
8
7
6
5
4
3
2
1
0
Type | Length | Message | Reserved 1
Reserved 2
Mobility Information
0
1
2
3

## Slide 5: Simulation Network Structure (1/2)

## Slide 6: Simulation Network Structure (2/2)
Two RSUs :
  Belong to one subnet.
  Connect with each other through Ethernet.
ffMultiple Vehicles :
  Driving through the road segment
Mobility Anchor:
  Manage RSUs and Vehicles.

## Slide 7: What got done
Setting up successfully a network with 3 RSUs
Mobility Information Exchange among vehicles
Coordinated maneuver when obstacle is detected

## Slide 8: What we learned
Lessons learned from this hackathon:
  To be able to exchange vehicle mobility over IP require an extensive modification of INET packets
  A coordinated algorithm orchestrates vehicles maneuvers to enhance road safety when obstacles are detected

## Slide 9: Wrap Up
Team members:
Champion:
  Jaehoon Paul Jeong (SKKU)
Students:
  Younghan Kim (SSU)
  Bien Aime Mugabarigira (SKKU)
  Yiwen Chris Shen (SKKU)
  Ahn Yoseop (SKKU)
  Kyoungjae Sun (SSU)
First timers @ IETF/Hackathon:
  Niket Agrawal (TU Delft)
  Kyungsik Kim (KNU)
  Park Jinho (KNU)
Video clip demo:
https://www.youtube.com/watch?v=6Ss5OzV88so
Where to get code (manual):
https://github.com/ipwave-hackathon-ietf/ipwave-hackathon-ietf-108