## Slide 1
IPWAVE Basic Protocols Project @ IETF-108 Hackathon
Champion: Jaehoon Paul Jeong pauljeong@skku.edu
Sungkyunkwan University
IETF 108, Online July 24, 2020

## Slide 2: IPWAVE Hackathon Project Poster

## Slide 3: Introduction
CNP Protocol for IP-Based Vehicular Network Motivation
  Use case of IPWAVE Problem Statement Document [draft-ietf-ipwave-vehicular-networking-16]
Subjects of This Draft
  Support the light-weight message exchange for vehicle safety
  Two-type message:
    Awareness: Cooperative Context Message (CCM)
    Emergency context: Emergency Context Message (ECM)

## Slide 4: Context Awareness in IP-Based Vehicular Networks
Context Awareness in IP based Network
Via lightweight messages Cooperative Context Messages (CCM)
Emergency Context Message (ECM)
CCM
ECM

## Slide 5: Vehicle Mobility Information (1/2)
VMI options:
Type
    Either: CCM and ECM
1
0
9
8
7
6
5
4
3
2
1
0
9
8
7
6
5
4
3
2
1
0
9
8
7
6
5
4
3
2
1
0
Type | Length | Message | Reserved 1
Reserved 2
Mobility Information
0
1
2
3

## Slide 6: Vehicle Mobility Information (2/2)
CCM
    Included in an NA message that a vehicle transmits periodically to announce its existence and routing information to its one-hop neighboring vehicles
ECM
    Included in an NA message that a vehicle transmits to immediately announce an emergency situation to its one-hop neighboring vehicles
ECM has a higher priority than the CCM
    If a vehicle has an ECM and a CCM to send, it SHOULD transmit the ECM earlier than the CCM

## Slide 7: Emergency Context-Awareness and response
Cooperative Context Message (CCM)
  Deliver a vehicle’s motion information
    Position, Speed, Acceleration/Deceleration, direction
    Diver’s action (e.g., braking and accelerating)
Emergency Context Message (ECM)
  Emergency situation notification
    Accident, dangerous situation
  ECM has higher priority over CCM

## Slide 8: Simulation Working Flow
OMNeT++
Veins (Vehicle in Network Simulation)
SUMO: Simulation of Urban Mobility
SUMO
OMNeT++
- Vehicle Speed
- Vehicle Lane
- Position...
- Vehicle Speed
- Vehicle Lane
- Position...
set
get
Algorithms
V-Local Sensing
V-Tracking Area: MCTA
Adaptation and
interaction
navigation scheme
Collision Risk
assessment
Response
algorithm
Motion planner
Context Awareness
Simulation scenario in veins: (ScenarioManagerLaunchd)
- Vehicle Speed
- Lanes
- Position
- Vehicle Speed
- Lanes
- Position
set
get
TRACI

## Slide 9: Road Network Architecture (1/2)
A 14*7 grid map with 3 lanes for a road network

## Slide 10: Road Network Architecture (2/2)
Two RSUs :
  Belong to one subnet.
  Connect with each other through Ethernet.
Mobility Anchor:
  Manage RSUs and Vehicles.
Multiple Vehicles :
  Driving through the road segment

## Slide 11: Vehicular Network Architecture
WAVE Stack
Vehicle Structure

## Slide 12
Proof of Concept (POC) of IPWAVE-CNP Protocol
  IPWAVE- Context-Aware Navigator Protocol (CNP)
Design and Implementation of IPWAVE-CNP in OMNeT++ and SUMO
  Design of IPWAVE-CND Framework in OMNeT++
  Implementation of IPv6 over IEEE 802.11-OCB
Proposal of Mobility Information sharing through Ligh-Weight packets in IPWAVE-CNP
  MI sharing through CCM and ECM Messages
  Coordinated Collision-Avoidance
Lessons from IETF-108 Hackathon Project

## Slide 13: Appendix
-Hackathon Development Environment
-Open-Source Depository of IPWAVE Basic Protocols Project
-Demonstration Video Clip of IPWAVE Basic Protocols Project

## Slide 14: Hackathon Development Environment

## Slide 15: Open-Source Depository of IPWAVE Basic Protocols Project
Github link:
https://github.com/ipwave-hackathon-ietf

## Slide 16: Demonstration Video Clip of IPWAVE Basic Protocols Project
Youtube link:
https://youtu.be/5OnpnYUiLhg